## Slide 1
CNN-Adaptive Sliding Mode Control
Autonomous differential-drive robots under environmental uncertainty
A DIGITAL TWIN APPROACH
Likhita Yerra · Mohamed Oussama Bouriga · Ahmed Ben Aissa · Abdellahi El Moustapha · Thibault Goutorbe
Supervisor · Prof. Vishvjit Thakar
PGE5 · AI Clinic · 31 August 2026
Notes: [Timing: 40 seconds]
Good morning. We are presenting our AI Clinic project on CNN-adaptive sliding mode control for autonomous differential-drive robots under environmental uncertainty. Our goal was not only to build a robust controller, but to create a complete and explainable AI-control pipeline—from environment perception to controller adaptation and a live 3D digital twin. The project was completed by our five-person team under the supervision of Professor Vishvjit Thakar. I will first explain the control problem, then the CNN and PPO approaches, show the quantitative results, and finish with the digital twin demonstration.

## Slide 2
The Defense in One Story
ROADMAP
PGE5 · AI Clinic · aivancity
02
01
Problem
Fixed SMC gains fail to balance accuracy and smoothness
02
Method
CNN recognises context and selects interpretable gains
03
Evidence
Five scenarios, four metrics, multiple baselines
04
Impact
Live digital twin makes performance visible and repeatable
TAKEAWAY The project connects robust control, explainable AI and an interactive digital twin.
Notes: [Timing: 35 seconds]
The presentation follows one simple story. First, a fixed-gain controller cannot respond optimally to every operating condition. Second, we use a CNN to identify the condition and choose an interpretable controller preset. Third, we evaluate that idea consistently across five scenarios and against several baselines. Finally, we expose the entire system through a live digital twin. This roadmap is important because the digital twin is not a separate interface; it is the final layer of the same research pipeline.

## Slide 3
One Controller, Conflicting Requirements
PROBLEM
PGE5 · AI Clinic · aivancity
03
Fixed-gain SMC
• Strong robustness to matched disturbances
• Simple closed-form control law
• Same gains in every environment
• Chattering–accuracy trade-off
Sensor noise
needs wider boundary layer and stronger smoothing
External push
needs faster heading recovery and higher correction gain
Wheel slip
needs larger surface gains to compensate velocity loss
TAKEAWAY A single static parameter set cannot optimise all operating regimes.
Notes: [Timing: 60 seconds]
Sliding mode control is a strong baseline because it is robust to disturbances and modelling errors. The limitation is that its behavior depends directly on fixed gains and the boundary-layer width. Sensor noise requires more smoothing to avoid rapid actuator switching. An external push requires more aggressive heading correction. Wheel slip requires stronger gains to recover the lost motion. These requirements conflict. If we tune only for noise, recovery becomes slower; if we tune only for disturbance rejection, chattering can increase. This is the central problem: one static parameter set cannot be optimal in all five environments.

## Slide 4
Research Gap & Contributions
INTRODUCTION
PGE5 · AI Clinic · aivancity
04
Research gap
SMC, CNN perception and reinforcement learning are well studied individually. Few compact, reproducible systems connect environment classification directly to interpretable SMC gain scheduling and evaluate the full chain in a digital twin.
1
Reproducible pipeline
Map generation → CNN → controller → evaluation
2
Explainable adaptation
Five classes mapped to hand-tuned gain presets
3
Multi-controller benchmark
Classical, fuzzy, CNN, oracle and PPO
4
Defense-ready digital twin
Live simulation, replay, compare and export
TAKEAWAY The novelty is the integrated, interpretable and demonstrable control pipeline.
Notes: [Timing: 55 seconds]
The individual technologies are not new by themselves. Sliding mode control, CNN perception and reinforcement learning each have a large literature. Our research gap is the integration of these pieces into one compact and reproducible system where the CNN does not replace the controller—it supervises it. That keeps the actual control law interpretable. Our four contributions are the full pipeline, scenario-aware gain presets, a multi-controller benchmark including an oracle upper bound, and a live digital twin that makes the research repeatable during the defense.

## Slide 5
From Perception to Control
ARCHITECTURE
PGE5 · AI Clinic · aivancity
05
Environment map
64×64 occupancy map
CNN classifier
5 scenario classes
Preset selector
λ, k, φ, αω
SMC controller
v and ω commands
Robot
differential drive
Alternative branch: PPO agent
Robot state + error → policy → adaptive SMC parameters
TAKEAWAY The CNN changes controller parameters—not the safety-critical control structure.
Notes: [Timing: 60 seconds]
This is the main system architecture. A grayscale occupancy map represents the operating condition. The lightweight CNN predicts one of five classes. That class selects a scenario-specific parameter preset containing the sliding-surface gains, velocity gains, boundary-layer width and angular smoothing. The SMC then calculates linear and angular velocity commands exactly as before. This distinction is important: the learned model is a supervisor, not an opaque end-to-end controller. The bottom branch shows our PPO alternative, which uses robot state and error to adapt parameters.

## Slide 6
Robot Model & Control Law
METHODOLOGY
PGE5 · AI Clinic · aivancity
06
Differential-drive kinematics
ẋ = v cos θ ẏ = v sin θ θ̇ = ω
State q = [x, y, θ, v, ω]ᵀ Δt = 0.01 s · wheel base L = 0.3 m
Sliding-mode control
Sliding surface
sᵢ = ėᵢ + λᵢeᵢ
Linear command
vᶜ = vʳ + kᵥdᶠ
Angular switching
ωraw = kω[ψ + tanh(sᵧ/φ) + 0.2 tanh(sθ/φ)]
Smoothing
ωᶜ = αωωᶜₖ₋₁ + (1−αω)ωraw
TAKEAWAY The boundary layer φ directly controls the robustness–chattering trade-off.
Notes: [Timing: 70 seconds]
The robot is modeled as a standard differential-drive unicycle. Its position evolves through linear speed v and heading through angular speed omega. The non-holonomic constraint means it cannot move sideways, so lateral pushes are challenging. On the control side, we define sliding surfaces from tracking error and its derivative. The linear command corrects forward error. The angular command combines bearing correction with smooth hyperbolic-tangent switching. Finally, exponential smoothing reduces high-frequency oscillation. The most important design variable is phi: a wider boundary layer reduces chattering but permits more steady-state error.

## Slide 7
Five Controlled Test Scenarios
EXPERIMENTAL DESIGN
PGE5 · AI Clinic · aivancity
07
01
Normal
No perturbation
02
Noise
Gaussian pose noise σxy = 0.02 m
03
Disturbance
Lateral push +0.4 m at t = 8 s
04
Slip
30% velocity reduction t = 10–14 s
05
Combined
Noise + push + slip
TAKEAWAY All controllers are evaluated under identical perturbations and timing.
Notes: [Timing: 45 seconds]
We use five controlled scenarios. Normal is the sanity check. Noise corrupts pose measurements. Disturbance applies a lateral push at eight seconds. Slip reduces effective velocity by thirty percent between ten and fourteen seconds. Combined applies all effects together and is therefore the hardest case. Every controller uses the same robot model, reference speed, simulation step and perturbation timing, so the comparison is fair. The normal scenario also verifies that adaptation does not introduce unnecessary behavior when no uncertainty exists.

## Slide 8
EnvironmentCNN: Lightweight Scenario Recognition
AI METHOD
PGE5 · AI Clinic · aivancity
08
Architecture
• Input: 1 × 64 × 64
• Conv blocks: 16 → 32 → 64
• BatchNorm + ReLU + MaxPool
• FC 4096 → 128 → 5
• ≈534k trainable parameters
100%
Simple maps
225 held-out test maps
95.1%
Realistic maps
walls, clutter & obstacles
5
Scenario classes
normal to combined
TAKEAWAY Classification is fast, interpretable and performed once before the mission.
Notes: [Timing: 65 seconds]
The CNN receives a sixty-four by sixty-four grayscale map. Each scenario has a distinct visual signature: a clean path, noisy pixels, an impact marker, a slip band, or all cues combined. The network has three convolutional blocks followed by a small classifier, for approximately five hundred and thirty-four thousand parameters. It reaches one hundred percent on the engineered test set. Because that dataset is deliberately separable, we also created more realistic cluttered maps; the CNN still reaches ninety-five point one percent. In deployment, one pre-mission inference selects the controller preset, so runtime cost is minimal.

## Slide 9
How the Presets Change Controller Behaviour
ADAPTIVE CONTROL
PGE5 · AI Clinic · aivancity
09
SCENARIO
PARAMETER LOGIC
CONTROL EFFECT
Normal
nominal gains
baseline behaviour
Noise
↑ φ, ↑ smoothing
less angular chattering
Disturbance
↑ λy, ↑ kω
faster heading recovery
Slip
↑ λx, ↑ λy
compensate velocity deficit
Combined
balanced preset
smoothness + correction
TAKEAWAY Adaptation remains explainable: each prediction maps to a documented engineering choice.
Notes: [Timing: 55 seconds]
This slide explains the system's interpretability. For each class we know exactly which parameters change and why. Under noise we widen phi and increase smoothing, which suppresses angular chattering. Under disturbance we increase lateral surface and angular correction gains, which improves recovery after the push. Under slip we raise both positional sliding gains to compensate for lost velocity. The combined preset balances these competing requirements. This is a key advantage over an end-to-end neural controller: every adaptation can be inspected, justified and bounded.

## Slide 10
PPO Agent: A Continuous-Learning Alternative
REINFORCEMENT LEARNING
PGE5 · AI Clinic · aivancity
10
Observation
error, rate, jitter, flags
Actor–critic
PPO + GAE
Action
select SMC preset
Reward
−error − jitter − effort
80k
Training steps
40 randomised episodes
0.2 s
Update interval
policy selects preset
48.9
Combined chatter
best in Table V
Promising, but weaker under disturbance and slip → more training needed
TAKEAWAY PPO is competitive under combined uncertainty but does not yet replace CNN supervision.
Notes: [Timing: 60 seconds]
We also implemented PPO as a learning-based comparison. The observation contains tracking error, error rate, a smoothed jitter measure and uncertainty flags. The actor-critic policy selects one of the same five SMC presets every zero point two seconds. Its reward penalizes error, chattering and control effort. After eighty thousand training steps, PPO reaches the lowest combined-scenario chattering value of forty-eight point nine. However, it performs worse under disturbance and slip. Therefore, our conclusion is balanced: PPO is promising, but the CNN supervisor is currently more reliable and more interpretable for this dataset.

## Slide 11
Evaluation Protocol
EXPERIMENTAL SETUP
PGE5 · AI Clinic · aivancity
11
DURATION
20 s · 2,000 steps
REFERENCE
straight path · 0.3 m/s
RANDOMNESS
fixed seeds for reproducibility
CONTROLLERS
Classical · Fuzzy · CNN · Oracle · RL
Four evaluation metrics
RMSE
overall tracking accuracy
Final error
post-perturbation recovery
Chattering
command smoothness
Control effort
actuator demand
TAKEAWAY Lower error is not enough: a useful controller must also be smooth and efficient.
Notes: [Timing: 45 seconds]
The main experiment lasts twenty seconds at a ten-millisecond time step. The robot tracks a straight reference at zero point three meters per second. Fixed seeds make the perturbations reproducible. We compare five controller variants, including an oracle that knows the true scenario and therefore defines the practical ceiling. We report four metrics because tracking error alone is incomplete. RMSE captures overall accuracy, final error measures recovery, chattering reflects actuator smoothness, and control effort reflects energy and mechanical demand.

## Slide 12
The Four Numbers to Remember
RESULTS
PGE5 · AI Clinic · aivancity
12
35.7%
Less chattering
noise scenario · 76.48 → 49.14
14.4%
Better final error
disturbance · 20.9 → 17.9 mm
32.7%
Better final error
wheel slip · 40.7 → 27.4 mm
95.1%
CNN accuracy
realistic cluttered maps
Near-oracle
17.9 mm CNN final error 15.6 mm oracle upper bound
Honest trade-off
Under persistent noise, smoother commands widen steady-state error—exactly as predicted by the Lyapunov boundary-layer analysis.
TAKEAWAY CNN adaptation improves the metric that matters most for each uncertainty type.
Notes: [Timing: 65 seconds]
These are the four numbers I want the panel to remember. Under noise, CNN adaptation reduces chattering by thirty-five point seven percent. After an external disturbance, final error improves by fourteen point four percent. Under wheel slip, final error improves by thirty-two point seven percent. On realistic maps, the classifier reaches ninety-five point one percent accuracy. In the disturbance test, CNN final error is only two point three millimeters above the oracle. We also report the limitation honestly: reducing noise-induced chattering increases steady-state error because of the wider boundary layer.

## Slide 13
Combined Scenario: Recovery After the Push
RESULTS
PGE5 · AI Clinic · aivancity
13
Read the graph
• Reference path: dashed
• Push at x ≈ 2.4 m
• Classical: largest overshoot
• CNN: tighter recovery
• RL: intermediate response
TAKEAWAY Adaptive controllers recover more tightly after the same impulsive disturbance.
Notes: [Timing: 55 seconds]
This figure shows the actual robot trajectories in the combined scenario. The dashed line is the desired path. Up to the push, the controllers remain close together. At approximately two point four meters, the lateral disturbance creates the sharp deviation. Classical SMC produces the largest overshoot and wider recovery loop. CNN-adaptive SMC returns more tightly because the disturbance preset increases heading correction. PPO lies between the two. The key point is that all three controllers receive the exact same disturbance; the difference comes from parameter adaptation.

## Slide 14
Combined Scenario: Error Through Time
RESULTS
PGE5 · AI Clinic · aivancity
14
Events
0–8 s
noise only
8 s
external push
10–14 s
wheel slip
14–20 s
recovery
TAKEAWAY The time series separates disturbance response, slip response and final recovery.
Notes: [Timing: 55 seconds]
The time-series view makes the experiment easier to interpret. During the first eight seconds, only measurement noise is active. At eight seconds, the external push causes an immediate error spike. From ten to fourteen seconds, wheel slip slows the robot and creates a second error increase. After fourteen seconds, all controllers recover. Classical SMC reaches the highest peak and remains above the adaptive methods for much of the recovery. This plot confirms that the trajectory difference is not a visual artifact; it corresponds to lower tracking error over time.

## Slide 15
Accuracy vs. Smoothness: The Real Trade-off
RESULTS
PGE5 · AI Clinic · aivancity
15
RMSE stays similar; combined case remains hardest.
CNN strongly reduces chattering under noise and combined.
TAKEAWAY The proposed controller trades a small RMSE change for much smoother actuation.
Notes: [Timing: 60 seconds]
These two charts must be read together. On the left, RMSE is similar between classical and CNN-adaptive control, and the combined scenario remains the hardest. Under noise, the adaptive controller accepts a small loss in precision. On the right, we see why: chattering falls dramatically under noise and combined uncertainty. This is not a free improvement; it is a deliberate engineering trade-off. Smoother angular commands protect actuators and reduce instability, while the controller preserves competitive tracking accuracy.

## Slide 16
Where CNN Adaptation Helps—and Where It Does Not
DISCUSSION
PGE5 · AI Clinic · aivancity
16
Interpretation
• Green = adaptive better
• Noise: major chattering win
• Disturbance/slip: final error win
• Red cells expose costs
• No claim of universal superiority
TAKEAWAY Adaptation is scenario-dependent—not uniformly better on every metric.
Notes: [Timing: 60 seconds]
The heatmap gives the most honest summary. Green means CNN-adaptive is better; red means worse. Under noise, the main benefit is smoothness, while final error increases. Under disturbance and slip, the main benefit is final recovery, while effort or chattering may increase because the controller becomes more aggressive. Under combined uncertainty, chattering improves strongly but RMSE changes very little. Therefore, our claim is not that CNN adaptation wins every cell. Our claim is that it makes the trade-off context-aware and explainable.

## Slide 17
Benchmark Against Fuzzy, Oracle and PPO
DISCUSSION
PGE5 · AI Clinic · aivancity
17
What it proves
• CNN ≈ oracle
• CNN beats fuzzy on key recovery metrics
• RL best on combined chatter
• RL weaker on slip
TAKEAWAY CNN supervision approaches oracle performance with lower deployment complexity.
Notes: [Timing: 55 seconds]
This benchmark provides context beyond the classical baseline. Fuzzy gain scheduling reduces noise chattering modestly, but CNN and oracle are clearly lower. Under disturbance, CNN reaches seventeen point nine millimeters compared with the oracle's fifteen point six. Under slip, CNN and oracle are nearly identical. PPO is best on combined chattering but weak under slip and disturbance. Overall, the CNN supervisor offers the strongest balance of performance, interpretability and low runtime cost.

## Slide 18
From Research Code to a Live Digital Twin
DEMONSTRATION
PGE5 · AI Clinic · aivancity
18
Demo sequence
1
Press T
Controller Tour
2
Compare
3-controller benchmark
3
Dual view
Classical vs CNN paths
4
Replay
Saved simulation
5
Export
Metrics as CSV
localhost:8000
TAKEAWAY The twin makes controller behaviour visible, comparable and replayable.
Notes: [Timing: 30 seconds, then switch to browser for 3–4 minutes]
This is the live digital twin. The left panel controls controller mode, scenario, trajectory and speed. The center visualizes the robot and its path in a hospital corridor. The right panel shows live metrics. I will now switch to the browser. First I press T to run the controller tour. Then I open Compare to benchmark all three controllers. If time allows, I show the dual path view and replay.
DEMO RECOVERY LINE: If the live demo fails, say: 'The system is also recorded here; this screenshot and the following quantitative results were generated by the same backend.'

## Slide 19
Limitations: What We Have Not Yet Proven
CRITICAL REFLECTION
PGE5 · AI Clinic · aivancity
19
1
Synthetic perception
Most maps are engineered; realistic set is procedural, not real LiDAR.
2
Pre-mission inference
Current CNN classifies once, not continuously during mission.
3
Hand-tuned presets
CNN chooses parameters but does not learn them end-to-end.
4
Simulation scope
2D kinematics, straight reference and fixed seeds.
5
RL maturity
PPO needs more training and reward shaping before deployment.
TAKEAWAY The results establish feasibility—not physical-robot generalisation.
Notes: [Timing: 50 seconds]
We want to be precise about the limits of the evidence. Most occupancy maps are synthetic, and the realistic set is still procedural rather than real LiDAR. The CNN currently classifies once before the mission. Parameter presets are hand-tuned, and the controller is evaluated in a two-dimensional kinematic simulation with fixed seeds. Finally, PPO remains an experimental extension. Therefore, this work demonstrates feasibility and a reproducible architecture; it does not yet prove generalisation to a physical robot or arbitrary terrain.

## Slide 20
Conclusion & Next Steps
CONCLUSION
PGE5 · AI Clinic · aivancity
20
What we demonstrated
• Context-aware SMC adaptation
• 35.7% chattering reduction
• Up to 32.7% recovery improvement
• 95.1% realistic-map classification
• Operational 3D digital twin
What comes next
• Real LiDAR occupancy maps
• Continuous online inference
• Monte-Carlo confidence intervals
• Longer PPO curriculum training
• Physical robot validation
TAKEAWAY Explainable AI can improve robust control without replacing the control law.
Notes: [Timing: 60 seconds]
To conclude, we built a complete perception-control-demonstration pipeline. The CNN makes sliding mode control context-aware without replacing its interpretable control law. The main evidence is a thirty-five point seven percent chattering reduction under noise, up to thirty-two point seven percent better final recovery, ninety-five point one percent classification on realistic maps, and a working digital twin. The next step is to move from procedural maps and fixed scenarios to real LiDAR, continuous online inference, Monte Carlo evaluation and a physical differential-drive robot. The core message is that explainable AI can improve robust control while preserving engineering transparency.

## Slide 21
Thank you
Questions & discussion
CNN-Adaptive SMC · PPO · Digital Twin
github.com/LikhitaYerra/smc_cnn
Supervisor · Prof. Vishvjit Thakar
Notes: [Timing: Q&A]
Thank you for your attention. We are ready for your questions.
LIKELY QUESTION — Why CNN if random forest is slightly better on realistic maps?
ANSWER: The CNN integrates naturally with image features and scales to richer spatial inputs. The random forest result confirms that the current cues are separable; the CNN is the extensible architecture for future LiDAR and camera maps.
LIKELY QUESTION — Is 100% accuracy overfitting?
ANSWER: It reflects engineered class separability, not real-world performance. That is why we separately report 95.1% on cluttered maps and state physical validation as future work.
LIKELY QUESTION — Why is CNN not better on every metric?
ANSWER: Smoothing and tracking precision conflict. The Lyapunov bound predicts that a wider boundary layer reduces chattering while widening steady-state error.
LIKELY QUESTION — Why not use PPO alone?
ANSWER: Current PPO is competitive on combined chattering but weaker under slip and disturbance. CNN supervision is more reliable, interpretable and cheaper at runtime.

## Slide 22
Backup: Scenario-Specific SMC Presets
APPENDIX
PGE5 · AI Clinic · aivancity
22
Parameter | Normal | Noise | Disturb. | Slip | Combined
λx | 2.00 | 2.00 | 2.15 | 2.20 | 2.15
λy | 2.00 | 2.10 | 2.30 | 2.20 | 2.35
λθ | 1.00 | 0.95 | 1.05 | 1.00 | 1.00
kv | 0.30 | 0.30 | 0.33 | 0.35 | 0.35
kω | 0.80 | 0.78 | 0.88 | 0.86 | 0.88
φ | 0.50 | 0.58 | 0.52 | 0.62 | 0.62
αω | 0.950 | 0.965 | 0.945 | 0.960 | 0.965
TAKEAWAY Preset values encode the engineering rationale shown on Slide 9.
Notes: [Backup slide — use only if asked about exact controller parameters]
These are the complete scenario-specific parameter values. Point out that noise raises phi and smoothing, disturbance raises lateral and angular correction, and slip raises both position gains. The combined preset is a compromise.

## Slide 23
Backup: Stability Argument
APPENDIX
PGE5 · AI Clinic · aivancity
23
V = ½(sₓ² + sᵧ² + sθ²) ≥ 0
V̇ ≤ −kω Σ sᵢ tanh(sᵢ/φ) + d̄ ‖s‖
V̇ < 0 outside a bounded region → sliding surfaces are uniformly ultimately bounded
Wider φ → lower chattering, larger ultimate tracking-error bound
TAKEAWAY The theory predicts the exact smoothness–accuracy trade-off observed in Results.
Notes: [Backup slide — use if asked about stability]
We use the composite Lyapunov function based on the three sliding surfaces. Because x times tanh of x over phi is positive away from zero, the derivative is negative outside a bounded disturbance-dependent region. This gives uniform ultimate boundedness. Inside the boundary layer, the error bound grows with phi. That is why noise smoothing reduces chattering but can increase steady-state error.

## Slide 24
Backup: Implementation & Reproducibility
APPENDIX
PGE5 · AI Clinic · aivancity
24
Simulation
Python · NumPy · Δt = 0.01 s
AI
PyTorch · EnvironmentCNN · PPO
Backend
FastAPI · WebSocket · REST export
Frontend
React · Three.js · Vite
Artifacts
models · CSV · replay · figures
TAKEAWAY One command launches the trained models, simulation API and digital twin.
Notes: [Backup slide — use if asked about implementation]
The simulation and evaluation are Python-based. PyTorch handles CNN and PPO. FastAPI streams state over WebSocket, while React and Three.js render the 3D twin. Runs can be recorded, replayed and exported. The project includes trained checkpoints and scripts for regeneration.